## Slide 1: EtherCAT Communication
Confidential 1

## Slide 2: Overview
Confidential 2
Introduction
Features
State Machine
Master
Slave Structure
Distributed Clocks and Synchronization
EtherCAT Network Information File (ENI)
Resources

## Slide 3: Introduction
EtherCAT
  Ethernet for Control Automation Technology
  A real-time Ethernet based fieldbus
  Developed by Beckhoff Automation
  Full-duplex of 100 Mbit/s BASE-TX
  Standard RJ45 connector

## Slide 4: EtherCAT Features
Master/Slave communication model
Processing data “on the fly” for cyclic data
Mailbox communication for acyclic data
Synchronization – Distributed Clocks (DC)
Flexible topology
Protocols
  CAN application protocol over EtherCAT (CoE)
  File transfer over EtherCAT(FoE)
  Servo drive profile over EtherCAT (SoE)

## Slide 5: Master/Slave Communication Model

## Slide 6: Processing Data “on the fly”
Process data is extracted and inserted on the fly
  https://en.wikipedia.org/wiki/File:EthercatOperatingPrinciple.webm

## Slide 7: EtherCAT Network Topology
  Star

## Slide 8: EtherCAT State Machine
Init
  Initial state after switching on
  No mailbox and process data communication
Pre-Operational(Pre-OP)
  Mailbox communication is possible
  No process data communication
Safe-Operational(Safe-OP)
  Mailbox and process data communication is possible
  Only inputs are evaluated but outputs are in “safe” mode
Operational (OP)
  Mailbox and process data communication is possible
  Inputs and outputs are valid
Bootstrap
  FoE

## Slide 9: EtherCAT State Machine

## Slide 10: EtherCAT Master
Software solution based by using either an on-board PC Ethernet controller or add-on network card
No special hardware is required
Two types
  Class A – standard EtherCAT master device with full features
  Class B – master device with limited features such as in embedded system with limited resources
Master Stack
  Acontis master stack running under RTX
EtherCAT network information file (ENI)

## Slide 11: EtherCAT Master Architecture (Acontis)

## Slide 12: EtherCAT Slave Structure
Each slave uses one EtherCAT slave controller (ESC) in the form of ASIC, FPGA or integrated in a standard microcontroller
EtherCAT slave information (ESI) file
  Each slave type comes with one EtherCAT slave information (ESI) file provided by vendor
  Contains the complete description of slave device network accessible properties
  Used by network configuration tool to configure the slave device

## Slide 13: EtherCAT Slave Controller (ESC)

## Slide 14: Frame Processing in the ESC

## Slide 15: EtherCAT Slave Address
Auto-Increment Address
  Each slave address is determined based on its physical position on the bus
Fixed Address
  The address of each slave is set by master in the configuration file
    Beckhoff hub device CU1128
  Slave may have secondary address (station alias). The address can be set on slave via two rotary switches or software
    Yaskawa SGDV.
    Rexroth IndraDrive
  The station alias address can be used to identify each slave

## Slide 16: Distributed Clocks (DC)
Synchronization of EtherCAT slaves
System time can be selected either 32-bit or 64-bit
The first DC capable slave is selected as a reference clock
Master cyclically distributes the reference clock value to other slaves

## Slide 17: Master Synchronization

## Slide 18: EtherCAT Network Configuration
EtherCAT Slave Information File (ESI)
  Provided by vendor
EtherCAT Configuration Tool
  The tool is used to generate EtherCAT network information file.
    EtherCAT Configurator (ET9000)
    TwinCAT
    Winmax EniBuilder
EtherCAT Network Information File (ENI)
  Describes network topology, initialization commands for each slave, PDO data mapping
  Used by master
  XML file based on a predefined file schema

## Slide 19: WinMax EtherCAT Architecture
Win32
RTX
Ethernet NIC (LAN1)
emllI8254x.rtdll
emllRTL8169.rtdll
Acontis Master Stack
EtherCAT.lib
WinMax RT
EcatScanBus.rtss
EcatFoeTool.rtss
EniBuilder.exe

## Slide 20: Resources
ETG
  www.ethercat.org
  UserName/Password: Hurco/h46268
Beckhoff
  www.beckhoff.com
Acontis
  www.acontis.com
Developer’s Corner
  RT\EtherCAT Technology