## Slide 1: EtherCAT SoE & FoE
Confidential 1

## Slide 2: Overview
Confidential 2
EtherCAT Communication Review
SoE
Sercos Basics
Rexroth IndraDrive
FoE
Resources

## Slide 3: EtherCAT Communication Review
Master/Slave communication model
Processing data “on the fly” for cyclic data
Mailbox communication for acyclic data
Synchronization – Distributed Clocks (DC)
EtherCAT State Machine

## Slide 4: EtherCAT State Machine

## Slide 5: SoE
SoE
  Servo Drive Profile or Sercos over EtherCAT
Sercos
  Serial real-time communication system
  Cyclic data channel
    Process data
    AT(Amplifier Telegram)
    MDT(Master Data Telegram)
  Acyclic data channel
    Read/Write parameters
    Procedure commands

## Slide 6: SoE Communication Phases

## Slide 7: Sercos Parameters
All operation data are mapped to parameters
Parameters are used for:
  Configuration
  Triggering and controlling drive functions and commands
  Exchanging data between master and slaves
Parameters can be identified via IDNs
Two types of parameters
  Standard parameters (S parameters)
  Product specific parameters (P parameters)

## Slide 8: Sercos IDNs
Identification Numbers
  Every IDN has an associated data block
  A data block consists of seven elements
    IDNumber
    Name
    Attribute
    Unit
    Minimum input
    Maximum input
    Operation data

## Slide 9: Sercos Procedure Commands
Commands are used to activate and control complex functions or monitoring features
  Drive control commands
  Monitor commands
  Administration commands
Each command is assigned to a parameter
Master can start, interrupt and clear a command

## Slide 10: A Procedure Command Example

## Slide 11: Device Internal State Machine
Parameter Mode(PM)
  Allows writing to all drive parameters which are not password-protected
Operating Mode(OM)
  Only allows writing to all drive parameters which can be changed in operation
Procedure commands
  S-0-0420, C0400 Activate parameterization level
  S-0-0422, C0200 Exit parameterization level

## Slide 12: Communication and Device State Machines

## Slide 13: Control Word S-0-0134

## Slide 14: Status Word S-0-0135

## Slide 15: Device Control State Machine

## Slide 16: Operation Modes
Supports up to 8 different operation modes
  Primary operation mode
  Secondary operation mode 1 to 7
Device control modes
  Torque/force control
  Velocity control
  Position control
  Synchronization modes

## Slide 17: Velocity Control

## Slide 18: Velocity Command Value: S-0-0036

## Slide 19: Rexroth IndraDrive
Hardware
  Power section
  Control section
Drive Firmware
  MPB - Single-axis with basic performance and functionality
  MPM - Double-axis drive with basic performance and functionality
  Multiple communication protocols are supported
  Licensed functional packages
  SoE is our default communication protocol

## Slide 20: Rexroth IndraDrive

## Slide 21: Rexroth IndraDrive MPM AT1 Mapping

## Slide 22: Rexroth IndraDrive MPM AT2 Mapping

## Slide 23: Rexroth IndraDrive MPM MDT1 Mapping

## Slide 24: Rexroth IndraDrive MPM MDT2 Mapping

## Slide 25: FoE
File Access over EtherCAT
  FoE file download
    Firmware
    Drive parameter file
  FoE file upload

## Slide 26: FoE File Download

## Slide 27: FoE File Download with Busy

## Slide 28: FoE Download with Error

## Slide 29: FoE File Upload

## Slide 30: WinMax Servo Layer
EcatMaster
SGDV
SD
RMB
Mitsubishi J4
Yaskawa
EcatSlave
RexIndraDrv
CoE
SoE
FoE
Master
Mailbox
Process Data
Distributed Clocks
Acontis Master Stack
NIC Driver
Master
EtherCAT Library
Rexroth
EcatIO
EcatServo

## Slide 31: EtherCAT Library Class Structure

## Slide 32: Resources
Sercos
  http://www.sercos.com/
User Manuals
  Rexroth Indra Drive
  Rexroth IndraWorks help manual
Developer’s Corner
  RT\EtherCAT Technology